SEE Report Week 1
Arka Mallick and Daiem Ali
Hochschule Bonn-Rhein-Sieg
12.04.2015

### 1. Experimental setup

 For the experiment purpose we build a simple robot with two wheels attached to motors and one free moving small wheel. For the marking of the starting and ending position we created a manipulator with a motor attached to it. The idea is to minimize the human error in the measuring process.

We programmed the robot to mark its starting position by rotating its arm at the beginning and then start executing the motion i.e. straight, left curve or right curve, when its done moving it rotate its arm again to mark th end position. This gives us a not a end point but also a vector in the direction of the movement as the arm is mounted parallel to the main chasis.

To ensure the identical starting positions we set up three Lego pieces to mark the starting position. See figure 1.1 and 1.2 for explanation.

Figure 1.1

Figure 1.2

In Figure 1.1 we can see the front view of the robot and in Figure 1.2 we can see the top view of the robot starting position. Where we can see the starting position of the robot is aligned with three sides to make sure the starting position remains same for all the experiments.

### 2. The robot program parameters used are as follows:
- we used DifferentialPilot Class for LEJOS NXT.
- Following input arguments were given to the DifferentialPilot.
  - Tier Diameter : 5.5cm
  - Track Width : 11.1cm (this is the distance between the two tires, taken from the middle of the tires.)
  - Reference of the left and right motors connected at robots port A and B of robot respectively.
- For moving the arm motor the NXTRegulatedMotor class was used, whit the motor port reference of port C.
- For forward motion the following parameters were used:
  - Travel distance 60cm.
  - Travel Speed of 10cm per second.
- For left and right angular motion:
  - Travel distance 60cm.
  - Travel Speed of 10cm per second.
  - Travel arc radius of 80 degrees for left arc motion and -80 degrees for right arc motion .
  - The program to run the robot is attached to this report (Main.java)

### 3. Observations made:
- Viewing from front, the right tire of the robot is tilted outwards which can cause the errors in the distance measurements of robots.
- The rear free wheel of robot displaces the robot a little to align itself to the direction of motion.
- When you run the robot for different distances it makes error proportionate to the commanded distance. e.g :
  - Commanded distance 50cm, achieved distance 50.5cm.
  - Commanded distance 20cm achieved distance 20.2cm.

In spite of making efforts to make the starting point exactly same, we found a set of marks by the manipulator which marks its starting position autonomously. Which indicates there were slight errors in the starting positions which contributed to the error in the ending positions.
### 4. The Observed data :

- We conducted the experiment 20 times for all three movements I.e straight line, left arc and right arc movement.
- The result of the experiments gave us one set of end point marks for each experiment.
- For the measurement of the coordinate we attached one frame to each of the set of data. And we marked the origin of the frames with relation to the starting point of the robot.
- Starting point is a point which we chose from the marks made by the manipulator as the starting point. (Ideally it should be just one point, but we actually have multiple marks very close to each other, but it portraits that the starting points also had some errors.)
- We assigned the coordinate values for each points in the local frame and recorded them.
- Then the values were transformed to the frame of the origin point.
- The measures are shown in mm and also in cms in the attached file (arka_daiem_datasheet_exp1)

### 5. Accuracy and Precision:

To analyse the data we created a python program. (arka_daiem_analyse_data.py).
The output of the program is as follows:
### Straight Line experiment
Mean Value X: 1.345
Mean Value Y: 58.925
x values range: -0.55 3.85
y values range: 58.6 59.55
Standard Deviation is: 1.28529179566
Standard Deviation is: 0.28788018341
### Right Arc experiment
Mean Value X: 17.6725
Mean Value Y: 48.6675
x values range: 16.0 19.5
y values range: 47.5 49.55
Standard Deviation is: 1.08402894334
Standard Deviation is: 0.610998158753
### Left Arc experiment
Mean Value X: -23.6975
Mean Value Y: 60.9675
x values range: -26.4 -21.1
y values range: 60.4 61.5
Standard Deviation is: 1.47075448325
Standard Deviation is: 0.380221974641

For the Range analysis we also did a outlier analyse but there was no outlier detected.
Comments:
To calculate the Accuracy we had to find the difference between actual point which it should reach and the mean Values obtained by our program. To obtain the Precsion the range analysis obtained by our program can be used.
The found results were plotted and attached to this report as .jpg files.